## Slide 1: Open Networking and SDN
PoWen, Tsai
Jan 2017

## Slide 2: Who am I
PoWen Tsai
  3 years Open Networking business experience in Edgecore
  Support Open Networking Business
      Pre-sales / Solution Planning
      Support NOS porting
      Post-sales technical support / RMA

## Slide 3: Mega Scale Operators (Facebook) DRIVING Industry Change
DISSAGREGATION
AUTOMATION
STANDARD DESIGNS
VIRTUALIZATION
FLEXIBILITY
Open Hardware
Software Control
Open Networking

## Slide 4: Open Compute Project (OCP)

## Slide 5: What’s inside a switch?
Control/Management Software
Network OS
Hardware Driver
Mechanical Box
Silicon

## Slide 6: Managing Switch as in Server way
Server
Switch
Customer Choice
Any OS on
Any Platform

## Slide 7: How to provision Bare Metal Switch like Server
Similar approach to installing OS on server
  BIOS + PXE → U-Boot + ONIE (Open Network Install Environment)
  Supported hardware (HCL) preloaded with ONIE
  ONIE available on GitHub
    http://onie.github.io/onie/
bare metal server
operating system
app
app
app
BIOS and PXE
bare metal switch
operating system
app
app
app
U-Boot and ONIE
Notes: Just like BIOS and PXE allows you to install an OS on a server using a remote image, the combination of U-Boot and ONIE allows that for bare metal switches.
We require ONIE preloaded on HCL because U-Boot is different across vendor devices, and U-Boot itself is not very user friendly.
We created ONIE and gave it to the Open Compute Project (OCP); it facilitates easy network OS installation of not just Cumulus Linux (Big Switch’s Switch Light OS is an example). Now you have your choice of installing whatever OS you want, not just what comes with the switch (e.g. Cisco IOS– OEM example, or FASTPATH– Broadcom’s OS).
Think of ONIE as PXE on steroids. ONIE is a small BusyBox Linux distribution, with a bunch of fetch and execution Bash scripts. It leverages modern ways of discovering networks using what was built into Linux—e.g., IPv6 neighbor discovery, DHCPv6, DHCPv4.
U-Boot is very good at probing the bus. U-Boot takes about 1MB. It has boot flash that’s dedicated to booting the hardware, separate from the Operating System flash. ONIE is a way to build on top of this. Takes about 3.5 MB.
ONIE is extremely well documented and flexible, and embraced by the open source community. (Source is on GitHub since summer 2013).

## Slide 8: Switch, Component Ecosystem and OCP Bare Metal
SDN Applications
Mgmt
Software
Network OS
Drivers
Box /
Mechanical
Silicon
Single
Vendor
Closed
Product
Traditional Networking
(Today)
ODM Chip
ODM Box
Open Source
Networking Stack
/NOS /
Control Plane Management Plane
Vendor
ODM Chip
Bare Metal
(Tomorrow)
ODM Box
Legacy Networking
(Past)
Single
Vendor
Closed
Product
“Black Box”

## Slide 9: Open Networking Software Ecosystem with Edgecore - Commercial NOS options
Cumulus Networks Cumulus Linux
  Linux NOS at web-scale with configuration, provisioning & monitoring tools
Big Switch Networks SwitchLight
  Big Monitoring Fabric and Big Cloud Fabric via centralized controller
Pica8 PicOS
  Hybrid Networking: OpenFlow 1.3/1.4 agent, with native L2 and L3 features
IP Infusion OcNOS
  Full function L2/L3 with MPLS/VPLS, Carrier Ethernet. OAM and telecom features

## Slide 10: Open Networking Software Ecosystem with Edgecore Open Source Software options
OpenSwitch
  Full function, open-source NOS
  Introduced October 2015 by HP with Accton as charter member; now under Linux Foundation
SnapRoute FlexSwitch
  L2 and L3 protocol suite, with comprehensive configuration APIs, automation and orchestration
  OCP Accepted
Open Network Linux
  OCP reference OS for switches
  Forwarding Agents: OF-DPA & Indigo OF Agent, SAI, OpenNSL, FBOSS Agent, Quagga Routing
Open Network Foundation Atrium SDN Distribution (CORD use case)
  OpenFlow physical (ONL with OF-DPA) and virtual switches
  ONOS open-source OpenFlow controller, with BGP application based on Quagga
Open Compute Project
  ONIE: Universal NOS Loader
  Switch Abstraction Interface (SAI): standard HAL for silicon from multiple vendors
  Open Optical Monitoring API
Software for Open Networking in the Cloud (SONiC)
  Network OS components, including full function L3 routing
  Contributed by Microsoft and co-contributors to OCP
SONiC

## Slide 11: CORD Architecture
R,E,M-Access
Metro
Router
ONOS Controller Cluster
vRouter
Control
vOLT
Control
Overlay
Control
Underlay Control
Multicast
Control
XOS (Orchestrator)
vSG
vSG
vSG
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
VNF
OVS
OVS
OVS
OVS
OVS
6712-32X
6712-32X
6712-32X
6712-32X
6712-32X
6712-32X
6712-32X
6712-32X
6712-32X
6712-32X
6712-32X
6712-32X
6712-32X
6712-32X
CORD-Fabric
Open Source
SDN-based
CLOS Networking
6712-32X
6712-32X
Residential
Mobile
Enterprise
Underlay
Overlay

## Slide 12
Open Networking
from
Freedom
Control
Innovation